## Slide 1: IVR finals
Images and Capture
Image Segmentation
Description of Segments
Simple Object Recognition
Active Vision
Sensing and acting
Reference Frames
Inverse Kinematics
Dynamics
Control

## Slide 2: Vision

## Slide 3: Images and Capture – Vision Basics
Difficulties in computer vision
  Viewpoint variation
  Illumination
  Scale
  Non-rigid deformation (same object in different positions)
  Occlusion (partially/fully hidden)
  Background clutter
  Intra-class variation of objects (eg different types of chairs)
  Inherent ambiguity (eg illusions)
Some basic physics/facts
  Human colour perception
    400 – 700 nm
    Three kinds of cones in the eye (RGB)
    More long and medium wave sensors – more perceptive of red and green
    Human eye is more sensitive to green light than red or blue
  Light depends on
    The light source: shape, position, colour
    The scene: shapes, surfaces, shadows, object colour, etc
    Sensor properties: camera properties, filters, etc
How imaging sensors/cameras work
  Each pixel of the camera captures photons
  Photons are converted to electrons, which are then shifted along the row and “collected” to be digitised
Color spaces
  RGB
    Linearly combined to produce all colours
    Good for computers but unnatural for humans
  HSV
    Hue: Colour
    Saturation: Paleness
    Value: Intensity/brightness
Aperture size
  Varies the amount of light captured on the film

## Slide 4: Images and Capture – Difficulties of Image Capture
Depth of field
  Different levels of focus for different depths
  Can use a smaller aperture to increase depth of focus; reduces the amount of light receives so need to compensate by using brighter light
Shadows & non-uniform illumination
  Increase ambient lighting using light diffusing panels, or many point lights
  Place illumination near the camera
Specularities/highlights
  Light reflecting off the object, straight into the camera
  Increase ambient lighting using light diffusing panels
Motion blur
  Use a shorter capture time (and brighter light to compensate)
Saturation problems
  Use a smaller aperture to reduce light, or reduce the gain
Radial lens distortion
  Straight lines captured as bent
  Use a more expensive lens, or view from a further distance
Aliasing
  Flickering lights at a certain frequency might cause bright and dark images
  Use incandescent light instead of fluorescent light

## Slide 5: Image and Capture – Projection
Projecting from 3D to image plane (2D)
  Not preserved
    Distance, angles and lengths
  Preserved
    Straight lines, incidence (intersecting lines)
Properties of projection
  Many-to-one mapping
    All points along the same ray of light map to the same point in the image (lost of info)
  Lines to lines
    Collinearity is preserved: things in a line remain as seen in a line
    Except for the line going through the focal point, maps to a single point
  Planes to planes
    All planes in 3D map to a plane in the image
    Except for the plane through the focal point, maps to a line
  Vanishing points
    All directions in 3D has a vanishing point in the image, where all lines in 3D in that direction converge at a point in 2D
    Except for the direction parallel to the image plane

## Slide 6: Image and Capture – Projection
Homogenous coordinates
  Homegenous image coordinates:
  Similar for homogenous scene coordinates (x,y,z)
Projection matrix
  P =
  To get image coordinates:
Homography
  A projection that maps points from one plane to another
  Accounts for 8 degrees of freedom
  Homography projection matrix
    Requires at least 4 matched points between the 2 planes
    Can be estimated using direct linear transform method
    Find least square estimate of P that satisfies the 4 equations

## Slide 7: Image Segmentation – Mean-Shift Clustering
Some common methods of region segmentation
  Contrast (light thresholding)
  Change: knowing the background, find the changes to identify the objects
  Similarity: grouping pixels by similar properties, eg colour clustering
Mean-shift clustering
  Mode: local maximum in a distribution
  Find the modes in a histogram using iterative mode search
    With a random seed and a window size W, calculate the center of gravity/”mean” of W
    Shift the search window to the mean
    Repeat this until mean converges
  Do a mean-shift at every data point, and find the attraction basin(s)
    Attraction basin: the region on the image where all trajectories point to the same mode
    Merge all the windows in that attraction basin (eg give them all the mean colour)
  Pros
    Easy to apply, model-free, only one parameter (W), robust to outliers
  Cons
    Dependent on W, which is not easy to choose
    Computationally expensive
    Does not scale well with dimension of feature space (eg mean-shift clustering with 2 features)

## Slide 8: Image Segmentation – Thresholding
Assuming pixel values are separable
Choose a threshold value that isolates dark and light peaks in the image histogram
  Assuming 2 big peaks
  Find the lowest point in the trough between the 2 peaks
Smoothing the histogram - convolution
  To better identify the peaks in the histogram
  Computed using a weighted sum of image data and a fixed mask
  1D and 2D convolution
  Also useful for edge detection, noise removal, etc

## Slide 9: Image Segmentation – Background Removal
Removing the background to find the change in image
Assuming camera is in a fixed position, before/after photos
Threshold the change in pixel value between the 2 images
  Can use on individual RGB channels
  Find the introduced object by OR-ing the threshold on the 3 channels
  To account for varying lighting/shadows, use normalised RGB representation
Background ratio isolation
  To deal with varying illumination
  Divide after image by before image
  If above or below a certain threshold, it is the object
  Note
    Darker = lower value, lighter = higher value

## Slide 10: Description of Segments – Simple Global Descriptors
Why descriptors: to identify an object’s class
Things you want in a descriptor
  Invariance to rigid transformation
    Does not change with translation, rotation and scaling
  Tolerance to non-rigid deformation
    Small variations are tolerated (could be due to manufacturing error)
  Point correspondence (not in this course)
Simple global descriptors
  Convexity
    Conv =
  Compactness
    How ‘circular’ the object is
    Comp =
  Elongation
    Distribution of pixels along the principal axes
    Ratio of long axis and short axis
  Pros: simple and fast to compute
  Cons
    Little discriminative power unless shapes are very different
    Do not deal with point correspondences
convex hull perimeter
shape perimeter

## Slide 11: Description of Segments – Moments as Descriptor
Moments: An infinite family of numerical shape descriptors
Can be made invariant to rigid transformations (trans/rot/scal)
Steps
  Calculate the area and center of mass of the image
  Get the first, ‘central’ moment
    Can use ANY u, v – infinite family
    Invariant to translations because taking the difference between center of mass position and the point position
  Make it scale invariant
  Make it rotation invariant
    Use a different formula for central momen (complex numbers)
    Make it scale invariant
    Calculate complex invariant moments
Feature vector
  Pack all the descriptors into a single vector to describe a single shape

## Slide 12: Description of Segments – Shape Signatures
Describing the boundary of a shape using a 1D function (a graph)
Centroid distance
  Distance from center of shape to the boundary
Curvature
  How curved each point is along the boundary
Can also use area, angles, etc
Pros
  Invariant to rigid deformation (if shape is normalised beforehand)
  Point correspondence
  Handles shape deformations to some degree
  Quite informative
Cons
  Sensitive to noise (especially for derivatives)
  High matching cost – where on the graph do you start?
Shape contexts
  Looks more at individual points and its neighbourhoods, match the most similar neighbourhoods between 2 objects
  Informative, invariant to translation, allows for some shape deformaties
  Invariant to scale if shape is normalised
  However, not invariant to rotation, computationally expensive, and requires many parameters

## Slide 13: Object Recognition – Intro
5 classes of object recognition algorithms
  Shape (similar shape descriptors)
  Appearance (similar pixel values)
  Geometric
  Graph
  Bag of words (similar local feature descriptors)
High-level shape-based recognition algorithm
  Extract object from image
  Compute properties
  Use properties to compute class
  Learning model’s properties for the class

## Slide 14: Object Recognition – Probability & Bayes Classifier
Finding the most probable of classes (relative probability)
  Given a feature vector x, measure p(class|x) for each class, find the most probable class
Bayes rule
Multivariate Gaussian Distribution
  Trying to factor out the dependence between feature variables (cross-correlation coefficient)
  Number of dimensions of Gaussian Distribution = number of features in feature vector
  Need 2 characteristics
    Mean vector: average value of the properties for the class C
    Covariance matrix: a matrix that takes into account the standard deviation of each property, and the cross-correlation coefficients between them
  Can use this model in the Bayes classifier
    Multivariate Gaussian Distribution gives the probability of observing x given a class, using the mean vector and covariance matrix
Need more training instances than number of features
  eg 4 samples needed for 3 features
  To ensure covariance matrix is invertible
  Obtain mean vector and covariance matrix from training instances
Using data set in training:
  Training set = ~50% (to estimate parameters)
  Validation set = ~25% (tells us when to stop estimating the paramters)
  Test set = ~25% (must be different to prevent overtraining)

## Slide 15: Object Recognition – Chamfer Matching
Matching and finding positions of objects with an error score
  Edges/boundaries must have been found in the image already (use an edge image)
  Ignores colour, lighting etc
Chamfer distance = average distance to the nearest edgel
  Edgel: a pixel in an image recognised as the edge of something
  Slide template over edge image and find the chamfer distance at each point
Distance transform
  Lookup table: shows the distance of each pixel to the nearest edgel
  Computing the distance transform is O(num of pixels)
  Slide template over distance transform instead of edge image
Pros
  Copes with cluttered images
  Can deal with small changes in scale, small amounts of deformation
  Works with fragmented edges
  Simple, fast
Cons
  Many false positive in cluttered regions
    Not smart matching
  Each different shape (variants or deformaties) needs a different mask, adds to computational complexity

## Slide 16: Active Vision
A sequence of images, like a video stream
  More information can be obtained more easily, such as depth, structure, location of object
Pros of active vision
  Obtain information such as depth, location, structure
  Can identify main object by comparing different images
  Can see object movement, analyse motion response of objects
  Can focus computer’s processing power on the main subject
Human vision
  Center of attention has highest resolution area
    If computer knows where center of attention is, can focus on that area, create impression of a complete, detailed scene
  Attention is drawn toward several image properties
    Orientation, size, colour
    Focus more on properties that are “salient” – noticeable
  Attention is drawn to motion
  Attention is given based on task
Motion can help reconstruct 3D object
  Parallax: displacement in apparent position of object when viewed from two different lines of sight
  Closer objects change apparent position more when we move

## Slide 17: Robotics
Sensing and acting
Reference Frames
Inverse Kinematics
Dynamics
Control
ROS basics

## Slide 18: Components of robots
Sensory components
  Acquiring information
Actuatory and effectory components
  Realising actions and behaviours
Information processing and control
  Processing signals, memory, planning and evaluation
  Open loop: no feedback
  Closed loop: feedback, maybe with touch or vision
Plus
  Batteries, interfaces, communication, etc

## Slide 19: Robotic Sensors & Actuators
Robotic Sensors
Purpose: location, objects and obstacles
Capabilities of sensors
  Distance sensing (vision, sound, smell)
  Contact sensing (taste, pressure, temperature)
  Internal sensing (balance, position, damage)
Classifying sensors
  Exteroceptive sensors
    Perceiving external objects; distance and contact
  Proprioceptive sensors
    Perceiving self movement and internal states
  Exproprioceptive sensors – combination
Alternative classification
  Active: emits energy (eg radar)
  Passive: receives energy (eg camera)

## Slide 20: Robotic Sensors & Actuators
Robotic Actuators
Effector
  Any device that has an impact on the environment (eg wheels, legs, grippers)
Actuator
  A mechanism that enables effectors to execute actions (eg motors)
Joints
  Rotary (rotation) or prismatic (linear motion)
Degrees of freedom
  Number of directions in which independent motion can occur (translation and rotation)
  Independent parameters that define the configuration of a robot
  2D: 3DOF (2 trans, 1 rot)
  3D: 6 DOF (3 trans, 3 rot)
Degrees of freedom of real world objects
  A rigid body (bodies in 3D) requires 6 DOF: 3 for position, 3 for orientation
  Human arm has 7 or 8 DOF
    Having more DOF than required makes it a redundant manipulator
    However, redundancy is useful for accommodating extra constraints, or doing tasks in a more optimal manner
Considerations when choosing actuators
  Load it can bear
  Speed, resolution (how specific)
  Accuracy, repeatability, reliability
  Power consumption, weight
Underactuated robot
  If DOF < number of joint parameters
  Can disregard some position parameters
Overactuated/redundant robot
  If DOF > parameters
  Will have more than 1 solution

## Slide 21: Task Space, Configuration Space, Reference Frames
Workspace aka task space
  Space of all possible positions the robot arm can move to
Configuration space
  Vector of all possible joint positions
  Vector space dimension = joint’s DOF
The kinematic model maps configuration space to task space
Reference Frames
A frame defined by 3 orthogonal unit vectors (axes)
Necessary to be established – inertial frame
  So that Newton’s Laws will take effect
  Can calculate position and orientation
Rotation matrix represents orientation of each new axes on the original axes
Always use right-hand coordinate system to define new coordinate system

## Slide 22: Rotation Matrices
Rotation can be parametrised by 3 angles
For each rotation about the x, y or z axis, will have an elementary matrix
  Multiply elementary matrices for a combination of rotations
Properties of all rotation matrices
  RT = R-1
    Useful for transforming coordinates back and forth frames
    Av = (RAB )(Bv)
    R-1 AB (Av) = RT (Av) = Bv
  det(R) = |R| = 1
    Rotation does not scale the vector
3 geometric meanings of the rotation matrix RAB
  Coordinate transformation from frame A to B (transform coordinates)
  An operation to rotate a vector (rotate vectors)
  Defines the three coordinate vectors of frame A with respect to frame B (define axes)
Euler angles
  Pick 3 angles (eg ZYZ, or roll-pitch-yaw), used to represent rotation to any orientation
  Can calculate rotation matrix from Euler angles, or Euler angles from rotation matrix
  Except in Gimbal Lock situation
    When you cannot get 3 angles from a 9-element matrix
    Happens when the second rotation angle (for ZYZ convention) is 0 or a multiple of pi
    1st and 3rd angle become coupled – cannot be uniquely determined/ lose one DOF

## Slide 23: Homogenous Transformations
Combining rotation and translation
  Distance moved given by , rotation matrix given by R3x3,
  For the coordinates p0 to p1
Combining transformations
  Can find the position and orientation of the robot in its task space as a function of its joint angles
    , where xe = end effector position, q = vector of joint variables
Denavit-Hartenberg Convention (D-H)
  A convention for defining reference frames
  Using only 4 parameters, can model robots and their transformation matrices in the simples possible way

## Slide 24: Jacobian Matrix & Inverse Kinematics
Jacobian
To compute the velocity of the end-effector wrt the velocity of the joints
  Differentiate with respect to time on both sides
  Jacobian J(q):
Singular configurations
  Configurations of q where J drops in rank
  Poses of the end-effector where end effector loses its natural rigidity, one of more DOF is lost
  Eg when theta 2 = 0 or pi
Rank of matrix
  Number of linearly independent rows
  Number of linearly indepdent columns (same)
Range space
  Set of all vectors spanned by the column vectors (task space)
Null space
  Set of all vectors such that Ax = 0
  Self-motion: joint motion that yields no end effector motion
Rank-nullity theorem
  Dimension of range space + dimension of null space = number of columns in matrix

## Slide 25: Jacobian Matrix & Inverse Kinematics
Inverse Kinematics
To find q, knowing xe
  However, problem if J-1 is not invertible
Dealing with overactuated robots
  Can optimise other things like kinetic energy of the robot
  Can also have robot meet secondary objectives like posture, work around an object
Dealing with non invertible J
  Pseudo-inverse
  Least squares solution:
    ‘Left hand pseudo inverse’
  Lagrange multipliers:
    ‘Right hand pseudo inverse’
Dealing with singularities
  Try to stay away from singularities
  Use damped least squares
  Use Jacobian transpose

## Slide 26: Static Equilibrium
Virtual work done
  Virtual work done by robot joints during an infinitesimal displacement
  Virtual work done by external force at end effector during that displacement
For static equilibrium, both have to be equal
Therefore,
  Joint torque = JacobianT x end-effector force

## Slide 27: Dynamics
Forward dynamics
  How the robot accelerates given applied forces and its state
  Calculate movement from force
  Useful for simulation and prediction
Inverse dynamics
  How much force we need to apply to generate a certain desired motion
  Calculate force from movement
  Useful for control

## Slide 28: PID Controller
A controller that generates input, to get an output
Error
  The difference between the output of the system and the desired value
Steady state error
  Where the error converges to, never reaches 0
  Normally occurs when the system needs a non-negative input for 0 error
Proportional (P)
  Present
  Using the error term to generate input with some gain/proportion (eg 5*error)
Integrator (I)
  Past
  Keeps a running total of the error over time
  To deal with steady state error – when total increases when there is steady state error, increases input such that error is driven down
Derivative (D)
  Future
  Measures the rate of change of error
  Prematurely decreases input if the error is rapidly changing so as to not overshoot the goal
Each branch (PID) has it’s own gain factor

## Slide 29: PID Controller – Choosing I
Is integral control useful or necessary?
  Not safe
    Wind-up effects
      Initial phase can lead to large values that result in unpredictable behaviour
      Any errors after the initial phase will be compensated
    Small gain factor usually used for precision
      This means a long reaction time, and therefore not good for tracking tasks
  Not necessary
    Only needed if steady state error is expected, or if system is noisy
  To mitigate these effects
    Reset integral
    Imperfect or time-windowed integration
    Disable the integral function until a certain region of error
    Initialise the integral at a suitable value
Another way to reduce steady state error
  Using a model to model gravity/etc (adding a constant instead of scaled term)

## Slide 30: PID Controller – K Characteristics
Characterising a control system
Stability
  Returning to the same point if there are small unintentional motions
Accuracy
  The difference between steady-state output and desired output
Settling time
  Time needed to converge to steady state
Rising time
  Time for the plant output to rise beyond 90% of the desired level for the first time
Overshoot
  How much higher the peak level is than steady state, normalised against steady state
Choosing gain factors
  Low gain – less energy used for control, precision
  High gain – faster response
Typically
  Kp to decrease rise time
  Ki to eliminate steady state error
  Kd to reduce overshoot and settling time
Effect of increasing K:

## Slide 31: PID Control – Limitations
Needs errors (an optimal value) to be able to react
Is only reactive and may be slow
D and I may suffer from sudden changes
D may suffer from intrinsic noise
  Use a low-pass filter
Is linear, not symmetric
  Cannot work both ways – eg increasing and decreasing the height of a propeller
Gain is tuned specifically to a systeme, unique to a system

## Slide 32: ROS
Robotic operating system: An OS that allows one to simulate and run robots in (soft) real-time
  Open-source and light-weight
  Simulators like Gazebo obey the laws of physics
  Allows for message passing
Communication in ROS
  Subscriber-publisher
    Node and topic
    Many to many
  Service-client
    One to one
Master node
  Manages the communication between nodes
  All nodes register at start up with the master
  Started with ‘roscore’
Node
  A piece of executable code
  All nodes communicate with the master node
Topic
  Nodes communicate over topics
  Each node can publish or subscribe to a topic
Service
  Services allow nodes to send a request and receive a response
  One time request: service node runs once then finishes
Messages
  Data that is published to a topic, that is ordered in a certain way
User interface rqt
  RQT – for GUI development in ROS, can be used to plot data, view images, node graphs, etc